Channels (including synapses)

I = G*(V-E), where G = Gmax*M^pm*H^ph;

Channel parameters
Local parameters	Global (shared) parameters	Common parameters
Gmax (generate once, different for different channel) / G (calculate every step) / GE (calculate every step) / I (calculate every step) / M (calculate every step) / H (calculate every step)	V (calculate every step) / E (calculate every step) / In ( calculate every step)	Parameters such as half-voltage, slope, time constant, etc for gate variables which are related to specific type of ions channel. / pm (generate once, different for different channels type) / ph (generate once, different for different channels type)

Ions dynapcis

E = Rtfz*ln( Out/In)
T*dIn/dt = -Rchan*Ichan-Rpump*Ipump
Ichan = SUM( G*(V-E))
Ipump = ???

Channel parameters
Local parameters	Global (shared) parameters	Common parameters
E (calculate every step) / In (calculate every step) / Out (calculate every step) / Ichan (calculate every step) / Ipump (calculate every step) / Rchan (generate once, different for different ions type or calculate every step) / Rpump (generate once, different for different ions type or calculate every step )	G (calculate every step) / E (calculate every step) / In ( calculate every step)	Parameters such as time constants, etc for ions dynamics which are related to specific type of ions. / T (generate once, different for different type of ions) / RTFz (generate once, different for different channels type)

Membrane potential

 C*dV/dt = -SUM( G*(V-E))+SUM(I)

Channel parameters
Local parameters	Global (shared) parameters	Common parameters
V (calculate every step) / C (generate once, different for different type of cell)	G (calculate every step) / E (calculate every step) / I ( calculate every step)